## Slide 1
Silvia Murgescu
Email: silvique_ms@yahoo.com
Lifter
Sky
Project Presentation

## Slide 2: Software Virtual Diagram
vMX
vSRX
Ubuntu Server
MacBook PRO
172.16.226.0/24
vmnet8 dhcp
.1
ge-0/0/0.0
.21
.10
fxp0.0
.20
eth0
INTERNET
Wireless Gateway
Software:
MacOS Sierra 10.12.6
VMWare Fusion 8.5.7
Ubuntu 14.4.1 LTS
vMX vmx-15.1F4-3
vSRX vSRX-12.1X47-D10.4-domestic
SecureCRT 8.1.3
Eclipse 4.6.3
Python 2.7.13 – PyEZ, JSNAPy
Git & GitHub
Silvia Murgescu
Email: silvique_ms@yahoo.com

## Slide 3: vMX Logical Diagram
vMX
ge-0/0/0 – ge-0/0/07
fxp0
Max 15 Logical Systems
Ubuntu Server
MacBook PRO
172.16.226.0/24
vmnet8 dhcp
.1
INTERNET
Wireless Gateway
.10
fxp0.0
.20
eth0
vMX Start
1. Connect to Ubuntu Server:
ssh silvia@172.16.226.20
password:
2. Initialize vMX router:
cd vmx-15.1F4-3/
sudo ./vmx.sh -lv --install
brctl show
sudo ./vmx.sh --bind-check
sudo ./vmx.sh --bind-dev
3. Connect to console and configure fxp0 interface:
sudo ./vmx.sh --console vcp vmx1
4. Connect to vMX Router:
ssh silvia@172.16.226.10
Silvia Murgescu
Email: silvique_ms@yahoo.com

## Slide 4: Network Diagram
MA-1001-1
MA-1001-2
MA-1001-3
MA-1001-4
MA-1002-5
MA-1002-4
MA-1002-3
MA-1002-2
MA-1002-1
PAG-1000-1
PAG-1000-2
AG-1000-1
AG-1000-2
Core-RR
L3 VPN Services
Customers
Access Network
Pre- Aggregation
Aggregation and Core
ISIS Area 1002 Level 2
ISIS Area 1001 Level 2
ISIS Area 0002 Level 1
ISIS Area 0001 Level 2
ISIS Level 2
Silvia Murgescu
Email: silvique_ms@yahoo.com

## Slide 5: IP Allocation
SP Network Class: 172.100.0.0/16
- Core area: 172.100.1.0/24
- Pre-Aggregation area: 172.100.2.0/24
- Access Area: 172.100.3.0/24
- Loopback interfaces: 172.100.255.0/24
- Network Services: 172.100.254.0/24
Services: 10.10.0.0/16
Customers: 192.170.0.0/16
Silvia Murgescu
Email: silvique_ms@yahoo.com

## Slide 6: Bibliography
Juniper JAUT course and lab
Day One: vMX Up and Running by Matt Dinham
Youtube: Git & GitHub Tutorial for Beginners by The Net Ninja
Juniper GitHub page: https://github.com/Juniper
Junos MPLS Application Features Guide, 2017.06.08
Universal Access and Aggregation Mobile Backhaul Design Guide

## Slide 7: Other Sources
Need a lot of resources
and vendor license
Silvia Murgescu
Email: silvique_ms@yahoo.com

## Slide 8: ICONS
vMX
vSRX
Use yellow glow for VIRTUAL PRODUCTS ONLY
L2-L3 Switch
Juniper Logical Router
Folder
Open Folder
Scripts
Ideas
Network
Automation
Laptop
Network Cloud
Network Lines are 1.5pt line weight
Network Cloud
Command Line Interface
Northstar Controller
Contrail vRouter
Contrail Controller
Junos Telemetry Interface
Third party product virtually running any Juniper software
Generic Server
Female Behind
Wireless Laptop
Wireless Gateway
Juniper Virtual Products
Juniper L2-L3 Switch
Silvia Murgescu
Email: silvique_ms@yahoo.com

## Slide 9
Lifter
Sky